## Slide 1: Design, Simulation, and Analysis of AM and FM Communication Systems
By: Justin Pulley

## Slide 2: Message and Carrier Signal (AM)
m(t) = Amsin(wmt)
Am Amplitude of Message Signal = 2
⍵m frequency of message signal = 2𝝅fm rad/s
fm frequency of message signal = 10 Hz

## Slide 3: Message and Carrier Signal (AM)
c(t) = Acsin(wct)
Ac Amplitude of Message Signal = 1
⍵c frequency of message signal = 2𝝅fc rad/s
fc frequency of carrier signal = 100 Hz

## Slide 4: AM Modulation
= Ac*(1+ 𝜇*m(t))*c(t)
Ac gain of carrier = 1
𝜇 modulation index = 1
m(t) message signal
c(t) carrier signal

## Slide 5: AM Demodulation (Squaring Technique)
= 𝐴c2(1+𝜇𝑚(𝑡))2 cos2(2𝜋𝑓𝑡)

## Slide 6: AM Noise Analysis
Added Additive White Gaussian noise at varying SNRs
The higher the SNR, the better the demodulated signal

## Slide 7: AM Bandwidth Analysis (B = 20 Hz)

## Slide 8: Power of AM Signal
Pc (power of carrier signal) = Ac2/2 = ½
Pf (total power of AM signal) = Pc(1+(𝜇2/2)) = ¾

## Slide 9: AM Overview

## Slide 10: Message and Carrier Signal (FM)
m(t) = Amcos(wmt)
Am Amplitude of Message Signal = 2
⍵m frequency of message signal = 2𝝅fm rad/s
fm frequency of message signal = 10 Hz

## Slide 11: Message and Carrier Signal (FM)
c(t) = Accos(wct)
Ac Amplitude of Message Signal = 1
⍵c frequency of message signal = 2𝝅fc rad/s
fc frequency of carrier signal = 100 Hz

## Slide 12: FM Modulation
= Accos(wct + (kf 0∫t(m(τ)*dτ))
Ac (gain of carrier) = 1
kf = 2𝝅 x 30
m(t) message signal

## Slide 13: FM Demodulation
Demodulates the FM waveform by modulating the Hilbert transform of the signal by a complex exponential of frequency -fc Hz and obtains the instantaneous frequency of the result.

## Slide 14: FM Noise Analysis
Added Additive White Gaussian noise at varying SNRs.
The higher the SNR, the better the demodulated signal.

## Slide 15: FM Bandwidth Analysis (B = 200 Hz)

## Slide 16: Power of FM Signal
FM does not affect the power of a signal, so the FM signal has the same power as the message signal.
B = Ac2/2 = 2 watts

## Slide 17: FM Overview

## Slide 18: AM vs. FM
FM signals use more bandwidth than AM signals.
Typically, FM signals are more resistant, but the results from my experiment shows that AM signals are more resistant.

## Slide 19: Questions?